## Slide 1: IBET GAME BASICS
Feb 15, 2024
Notes: This presentation outlines the purpose, design, and progress of the GAME bioreactor

## Slide 2
The GAME reactor selects for hydrogenotrophic methanogens to consume CO2 and H2
HYDROGENOTROPHIC METHANOGENS
HYDROGEN
EATING
METHANE
MAKERS

## Slide 3
Methanogenesis is the fourth step in anaerobic digestion
Complex organic matter: proteins, fats, carbohydrates, cellulose
Step 2. Acidogenesis
Soluble organic molecules: sugars, amino acids, fatty acids
Volatile fatty acids
Step 3. Acetogenesis
Acetic acid
Step 4. Methanogenesis
Step 1. Hydrolysis
Notes: https://biovoima.com/en/biogas

## Slide 4
Electron acceptors (oxidants) other than CO2 must be removed from the system to select for hydrogenotrophic methanogens
Lower Gibbs free energy of reaction (ΔG˚) indicates more energetically favorable reaction
Only feeding reduced forms of sulfate, iron, manganese, etc.
Notes: Sample mapping slide.
Reference:
Katrina Aspmo, Torunn Berg, and Grethe Wibetoe, “Atmospheric Mercury Depletion Events (AMDEs) in Polar Regions During Arctic Spring,” presentation (Oslo, Norway: University of Oslo, 16 June 2004).

## Slide 5
75% CH4
25% CO2
98% CH4
H2
HCO3-
The GAME bioreactor converts carbon dioxide from upstream anaerobic processes to methane
BIOGAS
98% CH4
CO2 gas dissolves in water
GAME
Hydrogenotrophic biomethanation
Mixed community anaerobic digester
Water alkaline electrolysis cell

## Slide 6
Limited solubility of H2 gas leads to inefficiencies in CH4 production
Solubility in Pure Water
CO2(g) : 0.169 g/100 mL
H2(g) : 0.00016 g/100 mL
Use molecular mass to convert to moles
0.0384 mol/L
0.000794 mol/L
But what does it mean?
≈48x
Molecules of H2(g)
Molecules of CO2(g)
Notes: Talk about diffusion kinetics
The speed at which these molecules diffuse into water prevents efficient consuption

## Slide 7
The relationship between pH and forms of dissolved CO2 determines whether CO2 escapes as gas
Image Source: importance of general chemistry relationships in water treatment mealy bowman

## Slide 8
HCO3-
H2
H2
H2
H2
HCO3-
HCO3-
H2
H2
The combined ERCHD and GAME reactor eliminates competitive dissolution of H2 and CO2 gas
BIOFILM FORMATION
Notes: Only have to worry about dissolving hydrogen – co2 already present, available, and abundant
Talk about diffusion kinetics